HOW USING A PNUEMATIC CAPSULE PIPELINE TO TRANSPORT COAL ORES AND OVERBURDEN CAN ELIMINATE THE NEED FOR DIESEL OR ELECTRIC POWERED HAUL TRUCKS AND THEIR RELATED EXPENSES AT THE BLACK THUNDER COAL MINE IN THE STATE OF WYOMING USA, AND LONG DISTANCE CONVEYORS AT OTHER SURFACE AND UNDERGROUND MINES.

Leon Edward Zaharis USA lzaharis@lightlink.com

ABSTRACT

The demand for sub-bituminous coal will continue to increase for

uses such as power generation, steel making, and coking coal

manufacturing, steam making for heating large buildings.

More of it will be burned to make steam and generate power than

with the burning of high sulfur eastern sub-bituminous coal. This

has required the design and building of larger and larger "Off The

Road" haulage trucks that have increased in size to carry up to 400

tons in payload. These haul trucks burn millions of gallons of

diesel fuel every year and must use very large rubber tires designed

specifically for their individual hauling capacities, these tires are

1

very expensive, costing more than $60,000.00 United States

dollars each. The machines are expensive to operate and maintain,

require large parts inventories and consumables, require extensive

driver training and have only a 50% rate of utilization due to

returning empty each time to the coal pit face for reloading for its

next load of low-sulfur coal. The modern capsule pipeline in use

today operates with little maintenance and is powered by

electricity. It pushes a high volume of low-pressure air stream and

uses the pressure gradient generated to push and pull the capsule

liners through the pipeline to their destination at 2,200 feet per

minute which is 25 miles per hour(40 kilometers per hour) or more

if more speed is desired. The loading and unloading system is fully

automated and operated by a personal computer.

One PCP system in operation since 1981 delivers broken limestone

ore from a  "Sumitomo Group" owned quarry to a "Sumitomo

Group" cement-making plant at the rate of two million tons per

year with an availability rate of over 90 percent. The system

2

operates with little maintenance and is powered by electricity,

pushing a high volume low pressure air stream, and uses the

pressure gradient generated by it to push and pull the capsule liners

through the pipeline to their destination at 2,200 feet per minute

which is twenty-five miles per hour or more if more speed is

desired. The loading and unloading system is fully automated and

operated by a personal computer.

The PCP system in use since 1981 delivers broken limestone to a

"Sumitomo Group" cement plant at the rate of two million tons per

year with an availability rate of over ninety percent. The system

in use there replaced a quarry-dedicated railroad. The pipeline

diameter is approximately 1.0 meter and has two tubes, one for

delivering limestone ore and a sister tube for returning empty

capsules to the quarries loading station. Larger diameter capsule

pipelines are fully capable of delivering millions of tons per year

of ore and even finished products in boxes, crates, containers or on

pallets, safely, economically over long distances as no diesel fuel is

3

required and operator labor is not required. The energy

intensiveness of large PCP systems has been shown to, in

BTU/TM (BTU energy consumed to transport each ton of cargo

over one mile of distance), has been shown to be in the

neighborhood of 100, which is about one-tenth of that of ordinary

trucks. This is based on a DOE sponsored study," An

Electromagnetic  pneumo capsule system for conveying minerals

and mine wastes," Final Report; DOE contract No. DE-FG-26-

03NT41928 (Author: Henry Liu And Charles W. Lenau) March 1,

2005.

4

1. INTRODUCTION

The increased demand for Wyoming low sulfur coal has put

pressure on surface strip mine operators to increase production and

railcar loading rates to meet new and old customer requirements

for cleaner burning low sulfur coal. This in turn has required the

designing and building of larger "OTR" (off the road) end dumping

haulage trucks to carry more coal in each trip from the mine pit to

the dumping station and returning empty to the pit face. These

trucks are sized from 100 to 400 tons payload weight or larger.

These machines use electric wheel drive methods.

Some Sub-Bituminous coal is extracted using large crawler

mounted draglines (which must remove the overburden to expose

the coal seam), electric mining shovels, and large front end

loaders. Some strip mine operators must use explosives to remove

the overburden by designing the mining pattern to cast the

overburden away from the area to be mined with large bench

mining and shooting techniques to expose the coal expose the coal

5

reserves. The coal is loaded into the waiting haul trucks to be

delivered to the crusher station where it is crushed, and carried by

a belt conveyor to a bulk storage or silo area for rail car loading

and later delivery to the customer by the railroad operating

companies serving the strip mine.

2. THE PROBLEM

The haul trucks return to the coal pit face "empty" to be reloaded,

and also burning diesel fuel unproductively in an empty haul back

mode with only a 50% utilization rate. This is done 24 hours per

day, 7 days per week 365 days per year in some of the coal strip

mines currently operating worldwide. A large haul truck fleet

requires large service shops,  a large labor pool for drivers and

mechanics, and a large amount of diesel fuel to power the trucks.

For example, a 100-ton haul truck may use over 500,000 gallons

of diesel fuel per year or more, oils, lubricants, and a large number

of spare parts. Moreover each fleet of trucks will require at least a

6

spare truck to replace the ones out of service, and the spare tire

inventory is also very expensive-a single off the road tire may cost

$60,000.00 or more. The "OTR" tire itself requires large mobile

machinery to mount and dismount it from the haul truck. The

training of the drivers of these haul trucks requires much expense

and time as well. Recently a number of companies are offering

computer powered driving simulator programs like the flight

simulator programs used to train airline and military pilots but the

problem of returning to the coal pit face empty each and every time

for another load still consumes 64 gallons per hour of diesel fuel

if a 100 ton (electric wheel drive)haul truck is used and more diesel

fuel when the larger haul trucks are used. If these employees are

are new surface mine employees in the United States there is also

the mandatory 24 hour training required by the Mine Safety And

Health Administration for surface miners and the annual 8 hour

refresher course related to the mining laws and procedures for the

United States.

7

3. UNDERSTANDING THE CAPSULE PIPELINE CONCEPT.

The pneumatic capsule pipeline (PCP) is based on the same

concept as a pneumatic tube which is a century old proven

technology using air pressure gradient to move capsules from

one point to another,  that pnuematic tube has been use for a  long

time in many areas such as banks, supermarkets, and parts

departments in factories. Even today, some pneumatic tubes are

used at drive in banks, large hospitals(such as the Johns Hopkins

Hospital), air port terminals and large factories. The modern PCP

takes advantage of a pressure gradient (3-5 psi) high volume air

stream for pressure and vacuum  to propel capsule trains at a speed

of  2,200 feet per minute or greater to and from its destination in

groups of up to five capsules from a loading point to the dumping

point and returning the capsule to the loading point in a pipeline.

At the Karasawa Mine at Kuuzu in Japan, a dedicated railroad car

transport system was replaced by a twin pipe capsule pipeline

nearly one meter in diameter(.998 meter) in 1981. Except for the

8

inlet and outlet the twin pipeline is buried under the old railroad

bed. At the quarry the capsules are batch loaded under a turntable

and then sent to their destination, dumped and returned to be

refilled with a fully automated batch loading system the same

described previously for loading that is computer controlled and

overseen by only one operator at the control center for the entire

PCP system.

The location for the Karasawa mine is:

1765, Aisawa, Kuuzu Town, Aso Gun, Tochigi Pref. Japan.

From Kuuzu Station (by Tobu Sano Line) ten minutes by car.

The Karasawa mine has a home page on the Internet as well.

The Karasawa mine telephone is 0283-86-2281

Products

(Limestone and Dolomite)

Raw material for cement       2,000,000 tons per year

Aggregate ………………     1,500,000 tons per year

Dolomite…………………..    700,000 tons per year

Total…………………….     4,200,000 tons per year

Ore reserves of more than 300,000,000 tons

9

The Karasawa Mine History

1937 Established as a limestone quarry for Tochigi Cement Plant of Fukoku Cement.

1963 changed into Karasawa Mine of Sumitomo Cement Co.LTD.

1981 capsule liner system established.

1985 B5-shaft (ore pass) completed.

1985 B5-Face installed-new mining area opened.

1994 Dolomite limestone plant established.

The broken limestone is loaded by mining shovel into a haul truck and hauled and dumped into the ore pass, crushed and stockpiled and then loaded into the delivery system and sent via the capsule pipeline to the cement plant.

A twin tube system is used to deliver the broken limestone in one tube and return the empty capsules in the second tube to the quarry. The capsule pipeline used at the Karasawa mine is almost one meter in diameter(.998) meter.

4. HOW THE CAPSULE PIPELINE ORE TRANSPORT  SYSTEM SOLVES THE PROBLEM OF ORE DELIVERY AT LOW COST TO THE USER.

The PCP method of ore transport is very efficient as it only uses a

low pressure high volume stream of air and vacuum to move the

capsule trains from the loading area to the unloading area and back

to the loading area. Each capsule of the PCP uses a close fitting

gasket that acts as a sail to propel the capsule through the pipeline

10

to its destination. Braking is accomplished by the front or leading

capsule in each train entering a sealed end tube air lock in a branch

Y creating resistance to the capsules flow in the tube. The capsules

enter in the end tube and come to a stop due to the build up of air

pressure in the tube in front of the capsule in a similar manner as

capsules entering a pneumatic shock absorber. The capsules are

captured with a locking mechanism and carried through the

loading /unloading system. The PCP method of transport has a

number of advantages over trains and trucks: it is unaffected by

weather, railroad crossings, slow traffic patterns, traffic or railroad

accidents, bad haulage roads, poor road visibility due to darkness

and snow storms and it does not require an operator to run them or

be affected by driver fatigue as the systems run by computer

operation, and no diesel fuel is used  The PCP uses electricity to

power the blowers used for pressure and vacuum service and

control systems, and it requires much less maintenance and many

fewer personnel than current methods of ore transport using haul

11

4. Continued.

trucks. The use of a linear induction motor (LIM) in a single pipe

system or a loop system can increase throughput capacities

eliminating the need for the air pressure pump bypass, which

hinders the free movement of capsules around the air pumps of the

PCP. Unlike blowers, which cannot pass capsules the LIM pump is

a non-intrusive pump that allows both air and capsule to pass

through the pump, thereby increasing the throughput and the

efficiency  of the PCP system. LIM are used to launch and act as

braking systems for the modern roller coasters, such as those used

at the Six Flags Amusement Park in St. Louis, Missouri. The linear

induction motor provides huge electromotive force to move the

modern roller coasters built today and they are used for many other

purposes requiring accurate positioning of materials in

manufacturing processes. I have provided several work sheets

describing the production capability of a 24 inch inside diameter

capsule pipeline with up to five individual tubes for a single pipe

12

delivery system method of delivery. The single tube system is the

least costly system to employ in operation from point to point.

(a) 7-mile-length system

I will describe a single 24-inch inside diameter seven miles in

length with an eight thousand foot long receiving tube on both

ends to store empty and full capsules, as well as a 14-mile loop

system and its production capability.

The actual capsule outside diameter is 22 inches to allow for pipe

clearances for a 24-inch inside diameter pipeline. Each capsule will

have a seal plate/rubber gasket to reduce airflow to reduce airflow

relative to the capsules, which makes the system more efficient and

nearly eliminating air blow by during the propulsion and vacuum

of the capsules during transport. The length of the individual

capsule is 72 inches plus the length of the wheel assemblies for this

assumption the wheel assembly  occupies one foot in length

making the length of the individual capsule to be 8 feet.

The capsule trains discussed are in units of five capsules with a

13

total length of forty feet. They can be grouped combining of a

number of capsules up to five units in length per train. Each

capsule  is  constructed of three-sixteenths inch thickness rolled

sheet steel attached to the wheel assembly disks. The interior of the

capsule hopper has several small gussets connecting the end discs

to the sheet steel tube to maintain rigidity and strength,  including a

Full-length gusset welded along the bottom interior of the capsule

at the six o clock position.  The single capsule volume is

determined by the formula for a right cylinder.

3.14 * 11*11*72 = 27,356 cubic inches- rounded to the nearest

inch,  which is 16 cubic feet rounded to the nearest cubic foot.

The volume for 5 capsules is 136,780 cubic inches or 79 cubic

feet-rounded. Assuming sub-bituminous coal weighs 52 pounds

per cubic foot the payload is 79 cubic feet times 52 pounds equals

4,116 pounds or slightly over two tons of payload per five car

train. Under the assumption that 200 five car capsule trains are

used in a single tube system the total payload in one transit is:

14

4,116*200=823,200 pounds, 411.6 tons per movement. If the trains

are batch loaded in ten second intervals six trains will be loaded

and shoved into the storage tube each minute. It will take 34

minutes to load and stack the 200 trains prior to launching the

group. If the trains are launched at 10 second intervals the first

train will cover the distance in 17 minutes by that time train

number 100 will have been launched into the tube to arrive at the

dumping point 17 minutes later, by that time train number 200

will have been launched and will arrive 17 minutes after that.

When train number 200 arrives and is dumped and pushed into the

receiving tube it will become train number one in the

launching and return sequence, to be loaded and stacked in the

filled capsule receiving tube again becoming train number 200 in

the launching sequence. The round trip will consume one hour and

forty two minutes not including the loading time when the capsules

arrive at the coal pit face. Under the assumption that a single

hopper is batch loading 6 trains  per minute and conveying them

15

into the storage tube for later launching the haulage time line upon

commissioning of the PCP system at midnight is:

12:00 train one is loaded and pushed into the storage tube.

12:01 train six is loaded and pushed into the storage tube

12:02 train 12 is loaded and pushed into the storage tube.

12:03 train 18 is loaded and pushed into the storage tube.

12:04 train 24 is loaded and pushed into the storage tube.

12:05 train 30 is loaded and pushed into the storage tube.

12:06 train 36 is loaded and pushed into the storage tube.

12:07 train 42 is loaded and pushed into the storage tube.

12:08 train 48 is loaded and pushed into the storage tube.

12:09 train 54 is loaded and pushed into the storage tube.

12:10 train 60 is loaded and pushed into the storage tube.

12:11 train 66 is loaded and pushed into the storage tube.

12:12 train 72 is loaded and pushed into the storage tube.

12:13 train 78 is loaded and pushed into the storage tube.

12:14 train 84 is loaded and pushed into the storage tube.

16

12:15 train 90 is loaded and pushed into the storage tube.

12:16 train 96 is loaded and pushed into the storage tube.

12:17 train 102 is loaded and pushed into the storage tube.

12:18 train 108 is loaded and pushed into the storage tube.

12:24 train 114 is loaded and pushed into the storage tube.

12:25 train 120 is loaded and pushed into the storage tube.

12:26 train 126 is loaded and pushed into the storage tube.

12:27 train 132 is loaded and pushed into the storage tube.

12:28 train 140 is loaded and pushed into the storage tube.

12:29 train 146 is loaded and pushed into the storage tube.

12:30 train 152 is loaded and pushed into the storage tube.

12:31 train 158 is loaded and pushed into the storage tube.

12:32 train 164 is loaded and pushed into the storage tube.

12:33 train 170 is loaded and pushed into the storage tube.

12:34 train 176 is loaded and pushed into the storage tube.

12:35 train 182 is loaded and pushed into the storage tube.

12:36 train 188 is loaded and pushed into the storage tube.

17

12:42 train 194 is loaded and pushed into the storage tube.

12: 42:30 the vacuum system is started creating suction within the

pipeline.  12:43 train (200) is loaded and launched in the pipeline

becoming train number (1) in the return sequence rather than

storing it.

12: 43:45 the second pressure blower is started creating back

pressure to drive the capsule trains to their destination in

combination with the vacuum blower at the dumping station.

The capsule trains are launched at 10 second intervals into the

pipeline being pulled by the vacuum at the dumping station and

pushed into the pipeline from the storage tube by the low

pressure air blown into the end of the storage tube by one of the

systems blowers. After train 200 hundred enters the tube train 1

will have reached the dumping station 17 minutes later and will

have been unloaded and  been pulled by vacuum into the rear of

the 8,000-foot storage tube.  Seventeen minutes later train 200 will

have arrived and been dumped and held in place on the dumping

18

station  becoming train number 1 for the return journey to the coal

pit face for reloading and return.

At 1:03:00 the vacuum blower at the coal pit face and the pressure

blower at the end of the storage tube are started to begin the return

empty trip. Train 1, which was train 200 in the delivery phase, is

released, and pulled by the vacuum created into the pipeline. The

199 trains in the storage tube follow train one for the return leg of

The trip. When train 200 enters the tube the second pressure

blower is started to assist delivery speed along with the blower in

the rear of the storage tube by remote control of the air or vacuum

delivery valves. Any and all dust created by the transport of the

coal is pushed by the air seals on the capsule trains and suctioned

into a cyclone system filter to be reclaimed and sold as coal dust in

the product stream..  It will require 2 hours and 34 minutes to load,

stack, launch, unload, return and reload the capsules for the second

round trip. Using the above time line including the reloading for

the return trip will allow for 9.35 trips per day, 65.45 trips per

19

week, 3,403 trips per year. The tonnage for 200 trains per trip is

411.6 ton's, which is 3,848.46 ton's per day, 26,939.22 tons per 7-

day week, 1,400,839.44 ton's per year. This is equivalent to

14,008.3944 load bearing trips and 14,008.3944 unloaded return

trips to the coal pit face using 100-ton payload haul trucks.

This is equivalent to 38.38 loaded and 38.38 unloaded return trips

per 24 hour day consuming 1,536 gallons of diesel fuel and 24

hours of labor per day; 10,752 gallons of diesel fuel per week,

using 168 hours of labor per week; 560,640 gallons of diesel fuel

consumed per year and 8760 hours of labor used yearly per 100 ton

haul truck.

(b) The seven mile loop system:

If a 14 mile " seven mile twin pipe" parallel loop system were

employed to carry crushed coal away from the coal pit face it could

be loaded and unloaded at a continuos rate of ten seconds for

loading and ten seconds for unloading. The parallel loop would

only require one unloading station where the five car capsule liners

20

would be received, rotated, dumped, air blasted to remove any

residual coal, rotated back to the upright position, slid over to the

return tube and sent back to the coal pit face for reloading. If the

system was filled to eighty percent  capacity it would require 1,478

five car trains and would be fully capable of loading and unloading

trains every ten seconds around the clock delivering  17,781.12

tons per day, 124,467.84 tons per 7 day week, 6,472,327.68 tons

per 365-day year in  single 24-inch twin pipe loop which is

equivalent to 64,723 loaded and 64,723 empty return trips to and

from the coal pit face with a 100-ton haul truck. The further the

coal pit face is in distance, the more capsule trains can be

employed to increase production from the coal pit face to the

unloading facility in any production plan to maintain a ten second

per capsule loading and unloading rate with no need for haul

trucks. The parallel twin pipe system would be attached to the

same wooden tie saving space and assembly time.

If two 7 mile twin pipe systems were used the production from the

21

coal pit face would double if an additional 1,478 capsule trains

were added to the system.

(c) A 36 inch-PCP system.

Using a larger inside diameter pipe system in a parallel loop or

single pipe system has many advantages as more ore can be carried

at one time in each capsule. In a 36-inch inside diameter pipe, a

single 34-inch by 72-inch long capsule can carry 1,966 pounds of

coal at 52 pounds per cubic foot. Five capsules in a train will carry

4.915 tons per loaded transit.  If a seven mile single pipe of 36-

inch inside diameter was employed to using the 34-inch diameter

capsule 72-inches long a 5-car PCP employing 200 trains it could

deliver 938.08 tons per loaded transit from the pit face to the

dumping station assuming a ten second loading time per train

200-five car 36-inch capsule liners making 9 round trips per day

will deliver 200 * 5 * 9.35 * 938.08 tons payload for 200 trains is

4,386 tons per 24 hour day, 30,699 tons per seven day week,

1,596,331 tons per 365-day operating year.

22

If a twin pipe parallel system were used as described above for the

24 inch pipe example the 36-inch pipe could have an eighty

percent fill rate with 1,478 five car capsule trains allowing loading

and unloading every ten seconds delivering 5.9 tons per

minute, 354 tons per hour, 8,493 tons per day, 59,452 tons per

seven day week, 3,091,495 tons per 365 day year. Doubling of the

number of tubes and capsule trains in an any production scenario

doubles production instantly. The tonnage above is equivalent to

30,915 loaded and 30,915 empty return trips to and from the coal

pit face with a 100-ton haul truck per year consuming 560,640

gallons of diesel fuel per haul truck 280,320 gallons is consumed

in "haul back mode consuming 32 gallons per hour) returning

empty to the pit face. 8,760 hours of labor per haul truck driving

full loads from the pit face 4,380 hours of which is used returning

to the coal pit face with an empty non-productive haul truck. The

50 % empty  haul back rate is the same no matter the size of the

haul truck or distance covered. Assuming a seven mile haulage

23

distance a 100-ton haul truck fleet will travel 216,405 miles with a

productive loads and 216,405 miles with no load returning to the

coal pit face consuming 64 gallons per hour per haul truck.

5. CHANGES AT THE COAL PIT MINING FACE.

(a) The current mining practices would continue with several

changes. The haul trucks would no longer be used and a large self

propelled hopper will be stationed at the pit face.

The self-propelled hopper will be carried by crawlers  to

move it from point to point at the pit face. The crawler drives

would be operated from one control station when needed and

the loading system operated remotely by the operator using the

mining shovel or drag line excavator. The hopper would receive

electric power from one of the nearby switch gears and

high voltage transformers for its use. The hopper would be sized

200 feet long, 40 feet wide and fifty feet high shaped as a trapezoid

and its capacity would be 170,000 cubic feet and could be smaller.

A 72 or 84 inch conveyor belt would feed a tripper belt with a pair

24

of ship trimmers to allow full filling of the hopper at all times. The

conveyor belt tripper would have an all weather operators cabin

allowing ease of  operation during bad weather. The tripper would

be equipped with high intensity discharge lighting for night time

use and times of  poor visibility. Positioned on one long edge of

the hopper there would be a "Carhoe" to clear blockages and

maintain flow to the 25 ore chute draw points under the hopper.

The "Carhoe" would be powered electrically and move with the

use of a rack and pinion drive system along the edge of the hopper.

The "Carhoe" would have an all weather cabin and high intensity

discharge lighting for nigh time use or during conditions of poor

visibility. The loading belt rising from the pit floor would have an

all weather cover over it to reduce blowing coal dust and a avoid

having a wet conveyor belt.  The head pulley and belt frame would

be carried by the hopper using slewing bearings. The belt drive and

take up would be under the frame of the conveyor structure

attached to the crawler and frame carrying the coal crusher and

25

apron feeder. A large apron feeder would be employed and

mounted near ground level on the crawler. The apron feeder will

deliver the coal dumped by the excavating machine into the hopper

above the crusher and after the coal is broken it will fall to the

conveyor belt and be carried up to the transfer point and then to the

tripper belt and dumped into the hopper. The hopper can be

designed to have as many as five loading lanes for the 24-inch

inside diameter pipe Five single pipe systems could be utilized to

deliver coal from the mine face using 25 five car capsule trains the

five single pipe systems will use five separate unloading stations

capable of unloading five trains at once and returning them all at

once to the loading lanes under the hopper. Five or six single pipe

systems could be utilized carrying 200 five a capsule trains per

tube at the starting point of the hopper in the mine plan. The

dumping station would require 5 additional  lengths of 8,000 feet

of pipe to store the 200 trains as they are emptied and ready to be

returned to the coal pit face.

26

At the pit face the front of the hopper would have five pipelines

exiting it to the right or left and these five  pipelines would carry

the 200 filled capsule trains and store them as they are loaded

under the hopper. Each tubes capsule trains could be launched at

the same time or separately delivering up to 1,000 loaded trains at

once to the coal dumping station and load out at one time

unloading up to 2,058 tons in one movement with a 24 inch inside

diameter PCP system. The same thing could be accomplished with

the 36" PCP system using four tubes and 800 five car trains and the

same thing could be accomplished using a forty two-inch inside

diameter pipe with 800 five car 40-inch capsule trains.

The coal pits pipelines eight thousand-foot length would be

extended every time the hopper moves to follow the mining

equipment. This will only occur when the conveyor feeding the

hopper has reached its maximum extended length. When the

mining shovel has reached nearly its maximum reach with the

conveyor feeding the hopper, the capsule loading system is shut

27

down. The mining shovel, front-end loader or crawler dragline

fills the hopper to its maximum capacity and then stops. The

mining shovel moves away from the front of the hopper to make

room for the pipe handling equipment and pipe carriers, which are

converted unused haul trucks with the dump beds removed and

pipe racks installed in the dump beds place. While all this is

happening the hopper is launching the 800 to 1,000 loaded trains in

all the storage tubes to the unloading station for unloading and they

will be sent back when the pipeline  work is completed for

reloading. After all the trains have cleared the storage pipes and the

hopper loading lanes the blowers are shut off on the loaded train

storage pipes.  If the four or five pipes are turned and travel in the

opposite direction of the hopper the curved sections of  the pipes

connecting the front of the hopper to the storage pipelines are

removed first. These sections of pipe are moved to the side of the

hopper with the bridge crane and carried away and set aside out

of the way of  traffic and any possible damage. The last eighty to

28

one hundred of feet of pipe is removed off the four or five the

filled capsule train storage tracks. The end caps are reinstalled with

the plumbing fittings for the blower and vacuum lines service. The

blower pressure connections and vacuum connections are

attached to the end of each pipeline.  The air control valves are left

on the hopper for ease of maintenance and to reduce plumbing in

the field. The check valves used to seal the system for either

vacuum or low pressure service are attached to the end T fitting

at the rear end of the pipe. The blower and vacuum piping used

is moved to the front of the line at the pit face for all the pipelines

and will be reconnected when the pipeline extension is finished.

seventeen minutes after the last trains leave the hopper loading

lanes the pipelines connecting the rear of the hopper are

disconnected and sealed with garbage bags and duct tape

maintaining clean pipe joints. At this time the pipe clamps and

gaskets are removed and put in a clean storage tool crib box on the

hopper-loading lane floor to be reused. After all the pipe joints

29

have been removed from the front and rear of the hopper the

hopper is moved forward the eighty or one hundred feet to allow

for connecting the pipeline extensions at the front and rear of the

hopper. The pipe carrier would carry 20 or 24 joints of complete

ready to install pipe panels on the rear of the carrier. The pipe

carrier would use a knuckle boom crane or jib crane to unload the

pipe panels near the hoppers bridge crane for ease of  installation

using the bridge crane for the pipe panels. The front and rear of the

hopper would have bridge cranes extending over the front and rear

ends of the hopper body to handle pipe and other items related to

the hopper such as replacement blower and vacuum packages,

removing individual capsules with damaged wheel sets to be

repaired and the carrying of the ore chutes and the three air

operated batch-loading gates to be installed under the hopper for

each loading chute for the individual capsule pipeline loading

lanes. The loading lane floor walkways would have metal grating

to eliminate coal dust and snow buildup and slippery floors from

30

rain and ice. The loading lane machinery and ore chutes would be

installed as the hopper is built from the bottom up as the hopper

can be constructed taking full advantage of open air construction

methods and the speed of system construction with open air

assembling of large machinery.  The ball park estimate I was given

for the cost of a hopper system this size with track drive was 80

million dollars plus or minus 15% from a P+H representative.

(b) There is also no reason a smaller high capacity self propelled

mobile crushing system could not be paired with the mining shovel

a smaller loading hopper feeding a twin pipe system. A Spokane

impact crusher could be paired with the self propelled crusher and

break the oversize and feed it into the smaller hopper loading

system. The smaller loading hopper would still be filling the

capsule trains at ten second intervals per train on a continuos basis

with any size capsule pipeline system or if a twin pipe system was

used or a single pipe system was used with longer storage tubes at

both ends of the system. The same rule still applies as the more

31

distance you have the more economical the system becomes to the

end-user. If a 42-inch twin pipe PCP system was employed with a

seven-mile starting distance and a pipeline fill rate of 80%

carrying 1,478 five car capsule trains. The sytem will be loading

and delivering 41 tons per minute, 2,460 tons per hour, 59,040 tons

per 24 hour day, 413,280 tons per week, 21,490,560 tons per year

to the railcar load out area  this is equivalent to 214,906 100-ton

truck loads per year all with out the use of haul trucks and diesel

fuel and only the use of electricity. The production rate can be

doubled simply by adding an additional 42 inch twin pipe system

and additional capsule trains. Larger positive displacement blowers

in blower and vacuum service would be required for larger a PCP.

(c) An even more productive PCP sytem employed in the

construction of the Akima Railroad tunnel for the Japan Rail

Company used in bullet train service could be employed.

This system was used to carry away tunnel spoil away from the

shielded tunnel boring machine and deliver ready mix concrete that

32

was dumped into a concrete pump that was used to fill a movable

form works following the shielded tunnel-boring machine.

The PCP was constructed of pre-stressed concrete panels that were

assembled to create a  pair of concrete tubes following the

shielded tunnel boring machine and the moveable concrete

form works used to create the tunnel lining for the twin train

sytem. The paired concrete tubes were assembled installed along

the side of the access road/rail bed to the tunnel to maintain a clear

path for the cement deliveries, construction company employees

and rescue vehicles if need. The ready mix plant was near the

tunnel entrance to facilitate the quick delivery of cement to the

constantly progressing form works lining the tunnel behind the

shielded tunnel-boring machine. One tube was use to remove the

tunnel spoil and carry it away to the nearby dumping site and the

second tube was used to deliver the ready mix concrete to the

mobile concrete form works. The pneumatic capsules were

designed as a rectangular shaped capsule with a hopper that

33

completely empties with straight sides and utilizing a fall away flat

bottom to empty to allow full ejecting of the tunnel spoil or ready

mix concrete. The spoil dumping point was set up with a gantry

system to allow the capsules to proceed to the end of the structure,

the bottom would drop away and eject the tunnel spoil in one quick

movement dumping the load completely with no residue remaining

to reduce the tonnage hauled to the spoil dumping point.

The capsules were retrieved and launched back to the ready mix

plant for filling with concrete for the moveable tunnel form works

following the shielded tunnel boring machine. The capsules were

designed with four rubber tires used to carry the capsule and with

four smaller rubber tires on the side of the hopper to center the

capsule within the tube to avoid contact and a possible collision

with the side of the tunnel. The end size of the rectangular capsule

was almost the exact size of the tube in cross section area to allow

suction and propulsion of the capsules to the interior of the tunnel

or to the spoil dump due to the rear or front of the capsule acting

like a ships sail.                            34

A concrete box culvert could be used to create the pneumatic tubes

at the black thunder mine instead of  a steel pipeline.

If a rectangular PCP was employed the system capacity will

increase significantly. A capsule 47.5 by 47.5 inches in cross

sectional area and 144 inches in length would carry 9,572 pounds

of sub-bituminous coal or 4 tons 1,572 pounds in one trip.

If the concrete box culvert PCP is filled to 80% capacity it would

be carrying 4,224 capsules being 1408 three car capsule trains

loading and unloading every ten seconds delivering  9,572 pounds

of coal every ten seconds, 57,432 pounds per minute, 3,445,920

pounds per hour being 1,723 tons per hour, 41,351 tons per 24

hour day, 289,457 tons per week, 15,051,779 tons per year. This is

equivalent to 150,518 100-ton truck loads and 150,518 empty

return trips and done without haul trucks or diesel fuel consumed

at 64 gallons per hour.  The capsule loading would be

accomplished using a carousel turntable batch loading system at

35

the loading point at the coal pit face similar to the sytem employed

at the "Karasawa Limestone Mine" used in batch loading their fleet

of capsule liners. Any residual coal dust would be carried in the air

stream to either end of the tube and be filtered out of the air

system. The maintenance of the capsule fleet is easily

accomplished as the capsules will be in full view at the loading

station and unloading station. The capsules can be removed easily

without disrupting production by guiding the damaged units to a

holding area or lifting them out of the ends of the loading or

unloading station where they are fully exposed for inspection.

The box culvert sections will be advanced one in front of the other

just as adding track panels are done with a railroad; no wiring will

be needed as the only place electricity will be needed is at the pit

face and the dumping area. The box culvert sections would have

gaskets to seal the ends of the culverts and the system could be

made air tight as well and allowing full use of the low pressure air

stream to push the capsules and vacuum to pull them to their end

36

points with ease simply due to the 6 general gas laws noted on the

following page and the fact that the payload weighs more than the capsule.

PERFECT GAS LAW

PV = nRT

P equals pressure in atmospheres.

V equals volume in liters.

n= number of moles

R= gas constant (0.0821 liter-atmosphere/K/mole)

T= temperature in K

If constant pressure           V1/V2=T1/T2

If constant temperature      P1/P2=V2/V!

If constant volume             P1/P2=T1/T2

Boyle's Law

If temperature is kept constant, the volume of a given mass of gas

is inversely proportional to the pressure which is exerted upon it.

Initial Pressure   equals   Final Volume

Final  Pressure                 Initial Volume

37

Charle's Law

If the initial pressure is constant, the volume of a given mass of gas

is directly proportional to the absolute temperature.

Dalton's law of partial pressures

The pressure which is exerted on the walls of a vessel is the sum of

the pressures of each gas if presented alone.

PV=V(P1+ P2+…Pn) these are ment to be P subscript 1 and P subscript 2)

Graham's law of Diffusion

Relative rates of diffusion of two gasses are inversely proportional to the square roots of their densities.

Avogadro's Law

Equal volumes of gasses, measured under the same conditions

of temperature and pressure, contain equal numbers of molecules.

Air velocity in a pipe

V = the square root of  25,000 DP divided by L

V= Velocity in feet per second

D= Pipe inside diameter in inches

L= Length of pipe in feet

38

Air volume discharged from a pipe

CFM = 60VA

CFM = air volume in cubic feet per minute.

V = air velocity in feet per second as determined in the equation

above.

A = the cross section area of the pipe in square feet

Theoretical horsepower to compress air

HP = 0.2267 Q [ PSI   + 1 ] 0.283 -1]

14.7

HP = theoretical horse power

Q   = system airflow rate in cubic feet per minute.

PSI= Outlet gauge pressure in pounds-force per square inch.

Conditions: (1) dry air at sea level atmospheric pressure = 14.7 PSI

(2) single stage adiabatic compressions

(d) A Linear induction motor system as described in Dr. Lius final

report to the Department of energy, mentioned previously can be

used in a box culvert PCP to propel the capsules back and forth

from the loading point to the dumping point if the capsules were

mounted on railroad wheel sets and used a narrow gauge railroad

track in the box culvert system overcoming the resistance of air

pressure in the tube to deliver full loads of coal and return the

39

empty capsules much faster than is possible with a blower system.

by using electromagnetism as he describes in his projects final

paper to the Department Of Energy.

(d) Many current and future mining operations both on the surface

and underground with long haulage distances from the mine face to

the railcar loading areas or stockpiles,  can and will benefit greatly

from the use of the Pnuematic Capsule Pipeline system due to its

simplicity and low maintenance and high through put capacities.

As long as the payload weight is greater than the weight of the

capsule carrying the ore the tare weight of the capsule liner it is

zero and no issue as the weight of the ore is what is being driven

by the air stream or pulled by the vacuum of a PCP system.

Any belt conveyor must be designed to carry a given tonnage of

ore per hour and the capacity to pull the weight of the belt and ore

at  the same time, at the same time the conveyor drive must pull

over troughing idlers through a conveyor drive unit over its head

pulley, through the drive pulley and back over the return idlers and

40

continue on to the tail pulley to repeat the trip.

The PCP system overcomes these issues simply due to the fact

that the entire system is in the pipe with no restrictions from idlers,

rollers, belting, skirt boards, impact idlers and impact bars at tail

pulleys. The PCP systems do not require the maintenance a belt

conveyor requires such as greasing idlers and main pulley bearings

oiling drive chains and gears checking gear cases and adding oil if

needed.   The conveyor belt requires reduction gearboxes or fluid

drive couplers high voltage power at every transfer point and

drive unit, belt splices to connect the lengths of belt together

conveyor belt speed switches and emergency stop pull cords the

entire length of the conveyor system, foundations for the drive

units and tail pulleys unless they are anchored to hard rock. The

conveyor belt must be trained to stay centered  in the troughing

idlers with permanently mounted training idlers and discreet

movements of troughing and return idlers. If the bearings in an

idler go bad the idlers must be moved and replaced. The hydraulic

41

take up unit pressure exerted on the belt used to maintain contact

and traction must be reduced on the conveyor belt to be able to lift

the belt above the idler, remove it,  and install a new one.

The idler must be aligned correctly or the belt will wander and be

damaged by over running the belt trough,  return idlers have the

same problem as well. The conveyor belt must be installed

properly as well. In recent years conveyor designs are allowing the

belt systems to curve  to follow terrain  and follow the right of way

for an overland belt. Conveyor belts must be inspected for wear

and bad belt splices being either vulcanized or mechanical, the tail

pulleys must be shoveled to eliminate build-ups of fines taken off

the bottom belt by the v plow in the front of the tail pulley and the

It must be done at the conveyor belt drive units as well as they

typically have belt scrapers under the head pulley.

None of the above maintenance, machinery or spare parts is

required with a pneumatic capsule pipeline system .

The PCP transport method of materials proven to work efficiently

42

at low cost in many applications. It has proven itself to be an

effective less costly method of removing tunnel spoil and

delivering ready mix concrete at the AKIMA railroad tunnel

project for the contractor excavating the tunnel and pouring the

tunnel lining and in the tunnels quick completion for the Japan Rail

Corporation.

(f) Any planned project such as the Mary River iron ore project in

Canada proposed by the Baffin land Iron Mines Corporation which

intends to deliver iron ore by rail from the mines to the planned

port 145 kilometers-90 statute miles from the mine properties

would benefit greatly from the use of a 24 inch capsule

pipeline system due to the systems simplicity and it can be run

around the clock 365 days a year delivering iron ore in the amounts

required without labor, and railroad hopper cars and locomotives

rail car rotary dumpers, rail car loading equipment and the fuel and

labor needed to operate the dedicated locomotives and hopper car

trains. The iron ore delivery system would only require a single

43

tube system due to its distance for transport and the weight of the

mined ore and eliminating the tare weight of a 24-inch capsule

liner to transport it.

With the Mary River iron ore projects desired tonnage of

12,600,000 tons per year the tonnage per day for a 365 day

delivery operation is 34,521 tons transported per 24-hour day.

If a 24-inch inside diameter pneumatic capsule pipeline was

installed for the delivery system it would  require two blowers

stations, one at the mine loading area and one at the port discharge

area the blower stations would require two packaged blowers each

using the model 624 Gardner Denver "Heliflow" blower; one used

for vacuum service and one used for pressure service at each

location. These blowers can and will deliver the vacuum of 16Hg

and low pressure air flow of 2,800 3,300 to CFM  at 5 psig or

greater needed to deliver the filled capsule liner trains and return

the empty ones between 3,167 CFM to 3,300 feet per minute at 16

Hg vacuum at a travel speed of 25 miles per hour or 40 kilometers

44

per hour. The capsule pipeline could be buried next to the

dedicated railway for the settlement  and mine taking full

advantage of the terrain used for the railroad.  The 24-inch PCP

would deliver 1,439 tons per hour 24 hours per day 365 days per

year unaffected by weather such snow storms, ice, high winds,

times of low visibility due to fog and rain, all without labor as

everything is in the pipe out of the weather and unaffected by the

weather. With a 365 day operating schedule fewer capsule trains

will be needed as a single capsule liner fleet could make one

journey per day and return in the same day.

Using the formula for a right cylinder:

3.14 * R*R*L

3.14 * 11* 11 * 96

for a single capsule capacity this gives us 4,243 cubic inches of

theoretical capacity in the capsule liner.  Allowing for the opening

to fill the capsule liner would reduce the volume slightly so using

20 cubic foot of iron ore would be the desired capacity per capsule

45

liner. Five capsule liners would be considered a train carrying 100

cubic feet at 201 pounds per cubic foot and the payload weight

would be  20,100 pounds per five car capsule liner train slightly

over 10 tons in payload per train. The capsule trains would be

loaded every ten seconds and it would require 24 minutes

to load and launch 144 five car capsule trains per hour for the

journey to the port to achieve the 365-day tonnage target.

It would require the building of 17,280 capsules for the PCP

system plus spares at the Baffin Land Iron Mines complex.

The capsules built for the PCP system at the Mary River site would

cost less to build than the rail cars needed as they require less steel

to build the capsules, they will weigh much less than the payload

weight of the iron ore and the tare weight of the individual capsule

will not be of any consequence as the iron ore weighs more than

the capsule, and the only weight being moved is the actual iron ore

payload weight. The first capsule liner train traveling at 2,200 feet

per minute would arrive 3 hours and 36 minutes later. The last

46

capsule train number 3,456 would arrive 9 hours and 36 minutes

later and be unloaded  The capsule liners would return to the mine

loading station  with the first train arriving ten hours later to be

reloaded for the return trip to the port to maintain the desired daily

tonnage of 34,521 tons per day operating 365 days per year using

no additional diesel fuel, labor or machinery delivering the iron ore

to the port for ship loading and returning to the mine load out. An

added benefit would be shipping of small freight packages and

mail in the pipeline to the mine as well using a sealed capsule to

allow for the clean delivery of small freight parcels and supplies

arriving at the mine. The tonnage required and the long nearly flat

distance of  the  path for ore delivery and return twin tubes will

allow easy installation to the mine and port and efficient operation. .

(g)A twin pipe PCP system can be buried below ground next to the

proposed railway line and will run continually delivering loaded

capsule trains to the port unaffected by inclement weather, sub-

freezing temperatures, poor visibility, high winds, derailments,

47

poor track conditions due to washouts, bearing failures on hopper

cars, broken connecting knuckles and main beams on the gondola

cars, air leaks in the braking systems and the brake pipes and

braking cylinders of the gondola car or cars, slack action damage

created by empty and loaded gondola cars impacting upon each

other, the need for replacing wheel sets, the main beam and springs

on the gondola car trucks. If a train derailment occurs the cars

damaged are quite often cut up and destroyed  and pushed to the

side of the right of way or scrapped. If an engine derailment occurs

during the derailment the possibility of major environmental

damage from fuel and oils spills is also a major negative factor

with the use of  rail transport. The weight of the iron ore itself will

be a major factor in building the railroad bed and the needed

drainage ditches to allow water to be carried away from the

railroad bed to maintain its rail road ballast profiles keeping the

rail road ties anchored to the railroad ballast bed. A twin pipe

system would need four of the Gardner Denver model 624 Heli-

48

Flow Blowers, two for vacuum service, and two for pressure

service. Each pipeline would have a blower set up for vacuum

service at opposite ends of the two pipeline and two blowers set up

for pressure service at opposite end of the pipelines.

(f) The delivery pipeline (Pipe1) carrying iron ore from the mine

loading station to the port would have a blower for pressure service

at the loading station to launch the capsules in the tube. At the port

(Pipe1) and the second blower is creating a pressure gradient to

pull the capsule liners to the port destination at twenty five miles

per hour or faster if desired to the dumping station where the

capsule liners are moved to the dumping station and then unloaded

by rotating them and allowing the loads to fall out, compressed air

may be used to blast the capsules clean of any sticking iron ore. A

poly liner could be installed to make the hopper a no stick surface

also. Then the cars are righted and sent along a small loop to (Pipe

2) where it is pushed into the pipeline and pushed into the low

pressure air steam delivered by the Gardner Denver Model 624-

49

Heliflow blower used in pressure service at the base of (Pipe 2). At

the other end of  Pipe 2) the Gardner Denver Model 624 Heliflow

blower is creating the pressure gradient to pull the capsules to the

mine for reloading and return to port with iron ore at a speed of  25

miles per hour(40 KPH) Essentially what we have created is a drag

strip in a pair of pipes with  pressure gradients at opposite ends

moving filled soda cans on wheels to either end at twenty-five

miles per hour (40 KPH) or faster if desired.

(g) A railroad car building company could build the capsules at

the port and be contracted to maintain the fleet with the available

local labor pool in the local as the rubber tires and wheel bearings

would need to be replaced as needed. A maintenance and repair

shop at the dumping station and at the loading station at the mining

area would take up little physical area near the loading and

unloading facilities.

50

51.  A basic drawing for the possible use of a twin pipe PCP at the Baffin Iron Mines Corporation Mary rive mine complex.

un

A concrete box culvert capsule pipeline twin tube system using

rectangular capsules rather than a large conveyor could be used to

move coal ore from a long wall coal mine face.

The placing of the capsule pipeline in the fresh air "inby" to the

long wall face or exhaust air "outby" will enhance the ability to

escape in the event of a fire or smoke condition as the culvert

would be a known secure pathway for egress from the mine face as

it would be a safe exit point to the surface protected from roof

falls. The PCP will not require railroad track or rail ties as the

capsules ride on rubber tires inside the concrete tube from the mine

face to the surface pushed by air pressure and pulled by vacuum.

The box culvert PCP system will not require any special equipment

as it is simply a reinforced concrete culvert section. It would be

possible to leave the PCP system in one position if the new ore

block is next to either the in by or out by where the PCP tubes are

located. The concrete culverts would act as an exhaust air conduit

to remove the bad air from the long-wall mine face due to the

52

pressure gradient created by transporting the capsules in the tube to

the surface. Large expansive room and pillar mines such as the two

salt mines in the State of Texas at Hockley, Texas and Grand

Saline Texas, the flat seam salt mines in Goderich, Ontario,

Magdelan Islands, Painesville, Ohio, Windsor Ontario, Pugwash,

Nova Scotia and Hampton Corners, New York, and salt domes at

Weeks Island and Cote Blanche, Louisiana would benefit as the

PCP system would allow them to carry salt faster and with less

expense and work than long distance conveyor belts and the

ventilation in the mines would improve greatly simply due to the

increase in air flow due to the use of the large blowers creating a

pressure gradient for ventilation increasing fresh air flow at the

mine face by 6,000 CFM or more with no additional effort using

the pressure gradient of the air flow in the tubes as an added

benefit as an additional air conduit for fresh air or exhaust air

without adding larger main fans to increase air flow. Mines with

long declines used as conveyor belt corridors would benefit as the

53

significantly simply due to the pressure gradient created in either a

twin pipe PCP or with a single pipe PCP system used to carry ores.

An added benefit is the ability to recoup some of the energy used

by capturing the exhaust from the vacuum blower and energizing a

vertical axis wind turbine with the air flow from its exhaust to

recapture the blower exhaust for energy manufacture using a

vertical axis wind turbine.

Unfortunately for the coal mining companies and other companies

that use haul trucks to move overburden spoil to access deposits of

valuable ores, and carry those ores for further processing the fact

remains that the haul truck is still under used by 50% due to the

fact that the haul truck always returns empty to the pit face or the

underground mine face in thick seam or dome mines so the

machine is unproductive fifty percent of its operating time and that

by itself has an effect on a mines operating expenses and net

potential revenues in a fiscal year.

54

This page illustrates the basic layout for a twin tube, four tube or five or six tube single pipe system without carousels diagramed for the twin and four pipe PCP

==========================================

55

This drawing is not to scale.

56

The basic layout for a single pipe system with loading carousel, capsule storing pipes, mobile crusher, coal loading conveyor, coal silo used to feed the carousel loading sytem.

The drawing is not to scale:

=========================================

57

The drawing is not to scale.

58

The following is the estimated cost for a single tube five thousand-foot Pneumatic Capsule Pipeline System

4 Gardner Denver Heliflow Blower packages  $200,000.00

8,800 wooden ties                                                 90,000.00

8,800 steel straps to anchor                                   88,000.00

pipe to wooden ties.

Pennsylvania crusher mountaineer sizer            $12,000,000

with a complete crawler system to carry sizer,

apron feeder hopper, loading carousel,

blower system at coal pit face.

single lane

LIM system for dumping station                        $500,000.00

to move and rotate 5 capsule liner

trains over dumping hopper

hopper                                                                   $20,000.00

Compressor and piping for capsule                      $30,000.00

cleaning at dumping station to remove

stuck coal from five capsule trains at once.

8,000 feet 24 inch OD pipe consisting of:

1,600 pipe joints estimated

.283 pipe thickness plus freight                               552,000.00

Additional pipe fittings                                            500,000.00

17,000 fine thread half inch by                             $   12,361.00

8 inch stainless Allen bolts,

17,000 Allen spring washers,

35, 000 half inch flat washers,

8,800 3/4 inch nylon lock nuts

59

One 24 inch pipe grooving machine                       $8,000.00

250-24 inch Victaulic pipe clamp joints             $327,000.00

2 pipe panel assembly jigs for assembling

each pipeline panel, price each                           $  20,000.00

The subtotal of almost $15,347,361.00 does not include labor for

installation and assembly for the system, crane service, taxes,

freight for components, fuel surcharges for delivery expenses,

generator rentals, legal expenses, temporary lodging and food

expenses for the installation crews etc.

The total could increase 50 percent with other possible expenses

and inflation or could be less. A PCP system will have expenses

relating to tire and bearing replacement on the capsule liners, any

blower repairs and maintenance for the blower systems used to

create the pressure gradients to push and pull the capsule line fleet

from the mine pit to the dumping station and back

The wear parts used in the carousel loading system if a carousel is

used to load the capsule trains with the replacement of the main

bearing on a loading carousel would take the most time due to the

need for a crane to lift the carousel up and away to replace a

60

complete main bearing.

If an overhead hopper mounted on tracks is used in combination

with an in pit breaker mounted crusher and take away conveyor the

the end product size would be ready for railcar loading. The in pit

expenses would relate to daily maintenance, replacement of idlers,

maintaining the "Carhoe", replacing wear parts in the loading lanes

relating to the guide ways under the loading chutes, electric

lighting repairs, the occasional replacement of the individual

loading gates over the loading lanes.

The PCP would occasionally require the replacement of a joining

gasket in a pipe joint for the PCP.  The PCP would advance as fast

as the mining shovel following the coal pit face and the carousel

or hopper loading system would take coal with no waiting from the

in pit crushing system. A mining shovel could feed an pit breaker

which in turn would feed a pair of 500 ton per hour electrified

Komatsu in pit crushers to deliver the final product to the capsule

loading system.

61

The above cost does not include the installation of a basic wireless

radio control remote operating system to operate up to 12 channels

for the system including the carousel operating system emergency

stop system, blower controls at the loading point etc.

About haul trucks:

Regarding the capital cost for a Caterpillar model 777 end dump

haul truck,  the base price is three million dollars excluding sales

taxes and freight expenses. This price does not include spare parts,

spare tires, the fuel cost for 500,000 gallons of diesel fuel to power

it per year, the oils and lubricants it will consume, the liability

insurance necessary for its operation at an open pit mine, the

operator training required to properly drive the machine at all times

and many other related expenses for its proper service at the open

pit mine where it is used. As with any mining operation operating

costs will increase with increases in fuel expenditures.

62

The drawings I have submitted for your inspection are for

preliminary designs for a linear loading and dumping system and a

carousel loading system and not draw to scale to display the

diameter of a loading carousel sized to fit one to six 40 foot long

capsule liner trains on a pass through batch loading turntable at one

time dump loading into one capsule liner at a time every ten

seconds.

Mr. Fiscors, thank you for allowing me to present this white paper

regarding the possible use of a Pnuematic Capsule Pipeline for the

transport of mined ores and overburden   I hope it is worthy of

being presented at the Haulage and Loading 2009 conference

meeting.

Leon Edward Zaharis

All rights reserved March 29, 2009.

63

This is a preliminary side view of the hopper loading system for

a rectangular crawler mounted hopper system without the crawlers.

coal pile inside hopper

The delivery belt from the pit floor is not illustrated

64

Hopper loading system continued;

Upon start up the first mass flow gates are closed and the bin is

filled. After a sufficient amount of ore is dumped into the hopper

the upper gate is opened to allow a predetermined amount of ore

above the closed second batch gate. The first gate is closed. The

second batch gate opens, and allows that ore to drop to the third

65

closed gate and the second batch control gate is closed.

The third batch gate opens and then the ore is dropped to the

closed forth gate. After the batch is dumped the third gate is closed

and the fourth gate opens to dump the measured batch to the fifth

gate. The fourth gate closes and that batch chamber is refilled.

The fifth gate, which is the pant leg bin is filled prior to the arrival

of the capsule trains in that loading lane. The final three dump

gates and chutes are sized to fill the individual capsule liner in each

system used in a system. The five capsule trains are loaded, shoved

back into delivery tube for launching or pushed into the stacking

tube for later launching depending upon the delivery system set up.

One air cannon is installed above the final loading gates in case of

ore plugging.

66

67

68

# Text boxes

pipe 1 delivering iron ore to  the port loading and stockpile area.

unloading station and port stock pile includes  the iron ore  unloading dump and loop to return empty capsule trains to pipe two for the return trip to the mine loading station

pipe 2 returning

empty capsules

trains to the

mine loading station

mine stockpile and loading station  utilizing a carousel large enough to load six trains per rotation  by batch loading and  move them to pipe one for the return to the port.

vacuum duty blower station for pipe one.

same as pipe 2

pressure blower station for pipe 2 same as pipe 1

pressure duty blower system for pipe 1

vacuum duty blower system for pipe 2

Pressure

service blower station for pipe 1

Gardner Denver

Heliflow Model 624

blower for pipe one 2,200-3300 CFM @ 5 -12 PSI.

The position of the twin pipelines is simply an illustration in the drawing.

in practice they would be buried next to each other in a properly bedded pipeline trench or mounted to concrete or wooden ties for the entire

distance except where they exited at the port

or mine stockpiles.

Vacuum service blower station for pipe 2

Gardner Denver Heliflow model 624 blower for pipe two

3,167 CFM at 16" Hg. vacuum.

Coal pit face area. face width is not to scale.

electric

mining shovel

self propelled tracked in pit roll sizer,  sized to electric mining

shovel capacity:

examples, Komatsu, Kawasaki,

Terex, Pegson,

etc.

Inclined

product belt exiting sizer to hopper and carousel loader

Overhead silo

for

carousel

loading system

Filled capsule train  storage tube exiting

carousel loader

PCP carousel

loading system

Apron feeder from silo to capsule loading carousel hopper

PCP exiting carousel loader to dumping station

pipe line route to dumping station

blower station for pressure gradient generation

CarHoe

Air pipelines from blower station

Hopper length

and width is not to scale.

PCP dumping station and railcar  loading area.

coal pit face

mining shovel

Primary breaker,  tracked in pit crusher

and take away belt follow electric mining shovel

in pit storage silo on crawlers

loading lanes are not shown. Both the loading and unloading lanes would use linear induction motors to move the capsule trains for loading and rotate the capsules for dumping and into storage for launching

to pit or dumping station

inclined conveyor to tripper above hopper

Carhoe on rack drive

on one long

side of hopper.

tripper belt

Depending upon the desired size of the hopper and the number of loading lanes, and whether storage tubes

exiting the pit face

are used on the pit face side of the hopper  for filled capsule liners prior to launching hundreds of capsules can be filled stacked and launched at one time to the mine load out area.

dumping station and  mine load out area

up to six loading lanes, singly or pairs

Moisture

drain

blower station for pnuematic capsule pipeline

air pipelines for pressure gradient generation

The silo could load 3 pairs of  24 inch PCP systems depending  on its width

using a sliding table to move filled and empty trains in large numbers at one time in a multiple twin pipe system

storage tube for empty capsule liners

moisture drain

pnuematic capsule liner travel direction to and from dumping station

The systems delivery direction can be reversed if needed with a few minor modifications

two way travel in single tube system the emptied capsules pass through the dumping station to the storage tube

linear induction motors can be used to move capsules through the dumping station for rotating and dumping payloads

to reduce equipment needs.

Carhoe boom and dipper arms

A twin pipe carousel system would have one pipe entering the carousel and one pipe exiting it on the opposite side returning

to the dumping station with a pipe loop returning to the coal pit face

pnuematic capsule liner travel direction

CarHoe crowding and dipper booms

Hopper  wind screen on both long sides

primary coal

chutes, five

chutes per

loading lane.

First mass flow loading gates for flood loading  the individual loading lane

Secondary batch gates

Tripper  belt

tripper control

Third batch control gate

tripperchuteschutes

left side ship trimmer facing you

Five loading gates per per capsule train for example

upper, middle and final batching gates for loading individual capsules

The last gates control the final flow to the capsule loading spout and prevent over filling, opening and closing in a one, two, three sequence after the capsule

train arrives under the pant leg bin to be loaded

Air cannons located here on all chutes

individual pantleg bins sized to capsule liner

opening

In pit conveyor

rising from pit floor

to hopper

elevated mobile hopper-

ore and overburden silo

Twin or triple

electrified

Komatsu in pit crushers

electric

mining

shovel

Hopper wall

slewing bearings for conveyor

incline conveyor

from pit floor

conveyor angle of attack  "X"

Conveyor drive

hydraulic take up and hydraulic power for crawlers under conveyor and crusher

Dumping hopper for twin or triple in pit crushers example

The twin or triple crusher example  uses a common hopper for dumping.

The crushers and hopper are carried

by a twin crawler unit not shown

Elevated in pit hopper

apron feeder tail end

Apron feeder head end

Hopper under apron feeder discharge

PCP loading carousel under hopper. the carousel is sized to fill any number of trains at one time the carousel has one common ore chute to fill all capsule train hoppers at each rotation

each individual  loading hopper  is sized to each capsule liners capacity and dumps into a common chute to

load each capsule

PCP entering under

carousel

5 loading

chutes

The pnuematic capsule pipeline is pushed through in a linear or circular path depending on the design of the loading system

and its size and available area.

chute to batch loaders

bottom discharge to loading carousel